Pyramidion software
Pierre FICHEUX (pierre.ficheux@smile.fr)

MODIFICATIONS

VERSION	DATE	AUTHOR	DESCRIPTION
1.1	10/4/2019	P. Ficheux	English version

# Introduction
This document describes the software of the Pyramidion control system (PHARES project) [1]. The software currently runs on a Raspberry Pi (or 0, B +, 3) but any other Linux system that can control GPIO may be suitable. The purpose of the system is to control the blinking of the leds in two cases:
with a frequency of 30 bpm (default behavior without sensor input) by "reproducing" a user's heart rate using a suitable sensor (Easy Pulse [2]) The system uses a GPIO output (led control) and two inputs (Easy Pulse sensor and manual / automatic switch).
The manual / automatic switch defines the operating mode:
- in manual mode the system runs continuously (flashing leds)
- in automatic mode the system starts / stops the service at fixed times (example: start at 19:00, end at 02:00) → use of the Linux “cron” service
A "master" system (with the Easy Pulse sensor) can also communicate the period to a "slave" remote system by transmitting the flash frequency in MQTT message. The two sites then flash at the same frequency.
# Technical description
Software is based on several components. The installed programs are different for the master and the slave.
## Software for “master”
- a program called gpioIrq (written in C language) and allowing direct control of GPIO (input and output)
- the pyramidion-gpio.sh script which runs the previous program with the correct options (GPIO numbers in and out, MQTT server address, and associated MQTT “topic”)
  $ gpioIrq -i $ GPIO_IN -o $ GPIO_OUT -h $ MQTT_SERVER -t $ MQTT_TOPIC
- a pyramidion-button.sh script that starts the cron, initializes the GPIOs and tests the manual / automatic state.
  - If the button is switched to "automatic" the GPIO service is stopped
  - If the button is switched to "manual" GPIO service is started
- a pyramidion-start.sh script called by "cron" → start GPIO service
- a pyramidion-stop.sh script called by "cron" → stop GPIO service
- a cron.tab file defining the start / stop times
- associated .service files (for systemd)

NOTES:
Switching to manual mode is not possible during automatic mode times if flashing is active.
If the mode is manual, starting by "cron" does not change anything but if we release the button the service is stopped even if we are in the time zone of the "cron" → do not forget to switch the button to automatic mode after use !!
The Easy Pulse sensor is not very "efficient". So the gpioIrq program waits 10 seconds before using the value of BPM obtained (stabilization) ! This value can be modified with the -w option of the gpioIrq program. At the end of the calculation, the program creates a thread to flash the leds with the calculated value of the BPM. This method provides a more regular flashing period than reproducing the value of the sensor (input) directly on the output (leds), which was done so far.
## Software for “slave”
- the rpi_gpio program (written in C language) which controls a GPIO with a given (half) period
- the pyramidion-receive.sh script that receives the frequency value from the master (by MQTT) and starts the rpi_gpio program. When starting the script, the led flashes at 30 bpm (default frequency).
- some additional .service files (for systemd)
# Configuring the Pi board
Currently the configuration of the board is manual from a Raspbian 9 (Stretch). The master board requires a saved clock (RTC) because the Pi does not have it by default. The necessary packages for the master and the slave are different, but for simplicity we will install the same on both targets with the following command.
$ sudo apt-get install mosquitto-clients libmosquitto-dev i2c-tools bc
## Installing “master” system
Compile and install the gpioIrq program:
$ cd gpioIrq
$ make
$ sudo make install

Copy the following scripts to /home/pi:
- pyramidion-button.service
- pyramidion-button.sh
- pyramidion-gpio.service
- pyramidion-gpio.sh
- pyramidion-gpio-start.sh
- pyramidion-gpio-stop.sh

Install and enable systemd services:
$ sudo cp * .service /etc/systemd/system
$ sudo systemctl enable pyramidion-button.service

Configure the "cron" file (file /home/pi/cron.tab) and load the configuration.
$ crontab cron.tab

The contents of the file is as follows:
# Format = min time day-of-month month day-week
#
# examples:
#
# 0 8 * * * -> every day at 8am
# 0 * * * * -> every hour
#
# Start at 7 pm, end at 2 am
00 19 * * * sudo ~ pi/pyramidion-gpio-start.sh
00 02 * * * sudo ~ pi/pyramidion-gpio-stop.sh

It is also necessary to configure the RTC [3] by following the link [4]. We sometimes had to add a 2 sec delay (using the sleep commang) to the file /etc/rc.local.
# RTC
echo "Setting RTC."
echo ds1307 0x68> /sys/class/i2c-adapter/i2c-1/new_device
sleep 2
hwclock -s
## Installing “slave” system
The configuration is much simpler because the slave receives the BPM frequency by MQTT.

Compile and install the rpi_gpio program:
$ cd rpi_gpio
$ make
$ sudo make install

Copy the following scripts to /home/pi:
- pyramidion-receive.service
- pyramidion-receive.sh

Install and enable systemd services:
$ sudo cp pyramidion-receive.service/etc/systemd/system
$ sudo systemctl enable pyramidion-receive.service
# Rest of work
Software specs have not been really written and the software has evolved day to day. The software is functional but was not deeply tested (just a few hours in simulation).
It is fundamental to write a test suite to detect boundary conditions. It should test the software over a long period (several days) and cause random state changes and errors.
In a second phase it is important to be able to configure the system without having Linux knowledge :
- software update
- configuring Wi-Fi network access
- etc.
Configuration could be done with a Web interface (in case of connected system). It could also be done with terminal (CLI) by updating configuration data that Raspberry Pi would download. In case of an off-line system, a local update could also be defined by using a USB key (or the Raspberry Pi could define a local Wi-Fi access point that can be used by a another computer).
# References